## Slide 2
Hutchinson group

## Slide 3
Hutchinson: activities
International leadership of industrial rubber
Sales Figure: €2,720M
12%
Fluid Transfer systems
Transmission and Mobility
24%
41%
23%
Sealing Systems
Insulation
Automotive
Heavy truck
All industry
Defense
Aerospace
Railroad
Notes: 25448 collaborateurs

## Slide 4
Hutchinson group
More than 100 worldwide production sites
More than 20 technical centers
1 corporate research center (Montargis, France)

## Slide 5
Measurements at Hutchinson R&D
Vibro-acoustic system modeling
Product improvement, ranking of solutions
Measurement/simulation comparison
Parametric studies
How to improve acoustic performance of automotive lateral windows

## Slide 6
Acoustic transparency measurement procedure
Mass law
Critical frequency

## Slide 7
Structure model
600×600 mm² plate glass
2-material glass run channel (2.2m long)
Aluminum frame (rigid)
Structural non linear 2D model (static analysis)
Structural analysis

## Slide 8
Structural 3D model (dynamic analysis)
Vibro-acoustic model
Coupled model
Baffled
Incident space : Rayleigh
Transmitted space : infinite FEM
600×600 mm² plate glass
2-material glass run channel (2.2m long)
Simulation by MSC/Actran
glass run channel
glass
incident
power
transmitted
power
air (I-FEM)

## Slide 9
Acoustic excitation
Diffuse field :
- same probability for every directions of plane waves
x
z
y
θ
φ
incidence (q) | number of azimuthal waves (j) | weighting of wave
0 | 1 | 0.2704
17.5 | 6 | 0.3095
35 | 10 | 0.3311
52.5 | 15 | 0.3180
70 | 18 | 0.3159
Total waves | 50 | 

## Slide 10
Transmission Loss per incident waves
Diffuse field :
- same probability for every directions of place waves
Real life measurement :
- truncation of some waves (wall proximity)
Truncation of waves gives higher TL
Glass thickness of 3,85 mm

## Slide 11
Transmitted power evaluation
Measurement of the transmitted acoustic power at 10cm from glass gives higher TL and critical frequency.
Glass thickness of 3,85 mm
Wtr

## Slide 12
Effect of glass thickness
TL is increased in LF as thickness is increased.
Critical frequency LF shift with thickness increase.
Higher TL at critical frequency for large thickness.
e

## Slide 13
Effect of glass run channel design
3 lips
2 lips
Effect at critical frequenncy
Ranking of glass run channel design
Glass thickness of 3,85 mm

## Slide 14
Product improvement
Several design proposals simulated
 Ranking of design proposal by simulation
Épaisseur de vitrage de 3,85 mm
most effective design

## Slide 15
Validated and reliable model that are used for:
  sensitivity studies on parameters such as thickness of the glass, design of the glass run channel
  comparison and ranking of different designs by simulation, allows less prototypes and tests
fine 3D mesh
Representative excitation
Computing of the transmitted power at the right location